## Slide 1: New Code Base
Paul Pridham
9/14/2022

## Slide 2: Overview

## Slide 3: Exo
Handles most of the computation
Configures System
Does primary sensor readings
  FSR
  Torque Sensors
Does primary output
  Motors
  Sync LED
  Status LED

## Slide 4: ExoData
Stores the data and parameters used to control the system
Mirrors setup of Exo

## Slide 5: Teensy
Handles most of the computation
Configures System
Does primary sensor readings
  FSR
  Torque Sensors
Does primary output
  Motors
  Sync LED
  Status LED

## Slide 6: SD Card
Stores system configuration
Till app fully set up:
  Contains parameter sets for different controllers.

## Slide 7: Motors
Currently CAN motors but other types can be added
Takes in torque commands

## Slide 8: Torque Sensors
Measures torques at the joint
Controllers have flag to use PID
  Select if torque sensor present
  Don’t use if there is no torque sensor

## Slide 9: FSR
Used to determine pressure at the heel and toe.
Used to determine foot strike and percent gait based on that.
Some controllers use one or both of these sensors.

## Slide 10: Status LED
Displays messages based on exoskeleton status.
  Colors (RGB)
  Patterns
    Solid (Color)
    Blink (Color, Freq)
    Pulse (Color, Freq)
    Rainbow (Freq)

## Slide 11: Sync LED
Used to synchronize the exoskeleton with infrared(IR) motion capture through an IR LED
Pulse Pattern
  Long pulse at start and end
  Small pulses in middle

## Slide 12: Nano
Handles Bluetooth communication
Mirrors ExoData stored on the Teensy
Handles low frequency sensor reading

## Slide 13: UI Host
Interface the user touches, app on phone or tablet
Packages and sends individual Bluetooth messages.